## Slide 1
Intro to {sherlock}: an R Package for Problem Diagnosis
by Gabor Szabo
SoCal RUG, April 18th, 2023

## Slide 2
Sr. Principal Engineer, Operations Excellence at Edwards Lifesciences
17 years of experience in engineering (quality and manufacturing)
Bachelors in Engineering Management
Have used R for 2 years
Data analysis
Shiny
Package development: sherlock
Taught fundamentals of R programming at Edwards Lifesciences
R for Engineering newsletter on LinkedIn
About Gabor Szabo

## Slide 3
Data analysis has always been my strong suit
From Excel to R to package development
Built custom applications in Excel
Tried to learn Python with no luck – haven’t given up yet
Stumbled upon R two years ago – love at first sight
Decided to build a set of functionality for my own use
The idea of a package
Development and submission

## Slide 4
Provides graphical and statistical tools for diagnosis of manufacturing-related problems
Small multiples types of visuals
Typically small datasets from experiments
Target audience: engineers who are tasked with diagnosing quality or performance-related problems of products, machines or processes existing in the physical world
Has been on CRAN since November 2022. Current version is 0.6.0
sherlock

## Slide 5
Important product characteristics
Customer level: safe, affordable, reliable, comfortable, attractive
Manufacturer level: form, fit, function
Product Quality and Reliability
Variation is the enemy
Raw materials, components
Processing
Environment

## Slide 6
Deviation from specified conditions
Problem needing resolution
Problem diagnosis – problem solving
Product Quality and Reliability
What drives variation in an important product characteristic?
Product quality and reliability
Problems prevented
Robust design (quality and reliability “designed in”)
Reactive
Proactive
Why did this problem occur?

## Slide 7
+
+
Causality in Manufacturing
Deterministic: laws of physics apply. Energy transformation.
Sparsity of effects: tells us that any effect cannot be evenly attributed to a large number of variables1.
Measured Values of a Product Characteristic (Y)
Variation in Parts
Variation in Measurements (Y)
Repeatability
Reproducibility
+
+
+
+
X17
X3
X6
X2
X11
X1
X20
Dominant X
1Diagnosing Performance and Reliability, David J. Hartshorne and The New Science of Fixing Things, 2019

## Slide 8
Diagnostic Approaches
Fishbone - Brainstorming
Hypothesis generators based on brainstorming and some amount of existing knowledge. The goal of a Fishbone exercise is to consider the potential impact of as many variables (Xs) as possible that we already know about or can think of. This approach, however, is not effective and is definitely not efficient.
Testing the effect of each of the potential variables may be possible, but most of it would be a waste of time and resources
Since these potential variables (Xs) are usually the result of brainstorming, a lot of times what we are searching for is not even on the list!
Consider how long it would take us to test the effect all of these potential causes; several weeks, if not months! We simply don’t have that much time.
What’s wrong?

## Slide 9
Diagnostic Approaches
Progressive search – Process of Elimination
In a progressive search, you start from the Y and converge on the X through posing and answering a series of questions
The questions must be phrased carefully so that all possibilities not yet eliminated are included thereby progressively reducing the search space – think binary search
What’s different?

## Slide 10
Diagnostic Approaches
Search Tree
Measurements
Parts
Elemental Variation
Higher Family Group
What drives variation in bond strength?
Cyclical Variation
Higher Family Group
Structural Variation
Temporal Variation
Inputs
Components
Function
Bonding process
Stopcock and tubing
Stopcock
Tubing
Interaction
Stopcock-Tubing
Stopcock inner cylindrical geometry: shape slightly elliptical at the bottom for cavities 5 and 6
Interference of stopcock ID and tubing OD

## Slide 11
Small Multiples
Data visualization technique
Coined by data visualization pioneer and educator Edward Tufte
Instead of plotting all observations from a dataset in the same space, they are grouped and displayed in separate smaller displays using the same axes and scale
“That is to say, nature’s laws are causal; they reveal themselves by comparison and difference, and they operate at every multi-variate space-time point” - Edward Tufte
Small multiples are codename for faceting in ggplot2
What’s different?

## Slide 12
sherlock - basic workflow
Import data
Plotting data
Data transformation
Report
Data cleaning / transformation
Simplicity

## Slide 13
Functionality

## Slide 14
Helper function for setting up a project folder
sherlock::create_project_folder()

## Slide 15
Wrapper functions around common functions for reading in .xlsx, .txt and .csv files
The ability to read in and clean multiple files (integration with a custom data cleaning function)
sherlock::load_file(), load_files()

## Slide 16
Small multiples plot
Takes a dataframe that includes the Y characteristic of interest and levels (groups) of X variables and outputs a multivari plot
Can handle up to 3 levels (groups)
Can be used with other helper functions such as draw_horizontal_reference_line() or normalize_observations()
sherlock::draw_multivari_plot()
ID at bottom
ID at tip

## Slide 17
sherlock::normalize_observations()
You can easily turn this…
Creates new column with normalized values
…into this!
Normalizing observations can be helpful to show deviation from an expected value, especially when multiple groups, each having a different expected value, are being plotted
Takes a dataframe and outputs a dataframe adding a column with observations normalized for the Y characteristic of interest
The new dataframe with the normalized values can then be plotted
ID at bottom
ID at tip

## Slide 18
sherlock::draw_polar_small_multiples()
Useful for plotting rotational or cylindrical data to understand shape or positional deviations
Information carried on the parts as to how their geometry is created1
1Diagnosing Performance and Reliability, David J. Hartshorne and The New Science of Fixing Things, 2019
Example 1: Shape of the inner cylinder of an injection molded component

## Slide 19
sherlock::draw_polar_small_multiples()
Example 2: Positional deviation of the two tips of a long, cylindrical component

## Slide 20
sherlock::draw_cartesian_small_multiples()
A powerful plot for visualizing data in a cartesian coordinate system (x-y)
Custom grouping and faceting
Full interactivity (built-in Plotly view)
Interactive Plotly Plot
Static Plot

## Slide 21
sherlock::draw_interaction_plot()
Used to visualize two-way interactions
Displays both main effects (means) and individual values

## Slide 22
sherlock::theme_sherlock()
Default
theme_sherlock()

## Slide 23
sherlock::scale_color_sherlock(), scale_fill_sherlock()
Default
scale_color_sherlock()

## Slide 24
Package Development

## Slide 25
Package development
Always design with the end user in mind
Standard argument naming conventions
Y variable
Grouping variables
Faceting variables
Aesthetics (color, alpha, size etc.)
Labels (x, y axis, subtitle etc.)
Interactive: Boolean
It is a software development project, and you are the developer, project manager, tester, technical writer, marketing specialist

## Slide 26
Thank you for your attention!
Connect with me on LinkedIn
https://github.com/gaboraszabo/sherlock
https://gaboraszabo.github.io/sherlock
install.packages(“sherlock”)